## Slide 1
Raster Datasets
Today’s Agenda
Hand back and review exam
Rasters
Map algebra and Boolean overlay
Other functions
Intro to Sand Table Project

## Slide 2: The raster data model
Raster Data Model: A method for representing instances of a field by dividing a space into cells.
Raster data models use a set of cells arranged in a grid pattern
Concepts or phenomena that vary over space

## Slide 3: The raster data model
4 key parts:
Number of columns
Number of rows
Origin (easting, northing)
Grid cell size (in ground units)
If you know one cell, you can get the location of any other feature

## Slide 4: Pixels or Cells
Each pixel contains one numeric value
Dimension of a pixel varies (resolution)
Value represents some property of that pixel area, for example, elevation or rainfall
Unlike a polygon, each cell has only ONE attribute: its value.
Storing multiple values means storing multiple rasters.

## Slide 5: Raster Properties

## Slide 6: Bands
A single raster may include multiple arrays
Most often used to store color images and satellite images
7-band Landsat satellite image

## Slide 7: Raster resolution
Measured by cell size dimensions
Storage space increases as the square of the resolution
Vector format
200 m raster
50 m raster
16x bigger!

## Slide 8: Cell size units
Cell x-y resolution units are based on the raster’s coordinate system definition
  Decimal degrees*
  Meters
  Feet
*Because distances and areas are fundamental to raster analysis, it is best to use projected coordinate systems for rasters.

## Slide 9: Raster analysis
Raster analysis uses cell-by-cell functions on one or more input grids.
Cells must be the same size and line up spatially.

## Slide 10: Raster analysis techniques
Map algebra and Boolean overlay
Other functions

## Slide 11: Map Algebra
Rasters are arrays of numbers
Can be added, subtracted, etc.
Line up matching cells vertically

## Slide 12: Map Algebra: Conversions

## Slide 13: Map Algebra: identify probable locations
Complex expressions with multiple inputs to calcuate risk or hazard index.
Runoff in cm based on four input grids: precip, slope, soil infiltration, and vegetation cover.
[Precip] * 2 + [Slope] * 4 / ( [Erode] – [Vegcover]

## Slide 14: Map Algebra: logical operators
Logical operators produce either TRUE (1) or FALSE (0) values in the output grid, based on whether a cell meets the condition.
[Elevation] > 1200
[Slope] < 10
[crowncov] < 70 AND [crowncov] > 40

## Slide 15: Boolean rasters
Boolean rasters represent maps of True/False states for a particular condition
Slope < 10 degrees?

## Slide 16: Boolean overlay (AND)
[PrecipGT60] AND [ElevGT1500]

## Slide 17: Additive Boolean overlay
ADD the layers together to create a ranked result.

## Slide 18: Raster analysis example
Siting a landfill

## Slide 19: Landfill raster model
Problem: Find potential locations for a new landfill using these criteria
  On flat terrain <= 10 degrees slope
  No more than 1 km from an existing road
  At least 500 meters from a stream
  Meadow or low-density forest
Develop a Boolean raster for each condition with 1 = desirable area, 0 = not desirable area

## Slide 20: Landfill suitability index (LSI)

## Slide 21: Slope condition
Use slope function on elevation raster.
Use map algebra logical operator to produce Boolean map of slope <= 10 degrees.

## Slide 22: Road distance condition
Use distance function to create raster of distance from roads.
Use logical operator in map algebra to create Boolean raster of areas within 1000 meters of a road.

## Slide 23: Stream distance condition
Use distance function to create raster of distance from streams.
Use a logical operator in map algebra to create a Boolean map of areas more than 500 meters from a stream.

## Slide 24: Vegetation condition
Select suitable vegetation density and create a layer from the selected polygons.
Convert the selected vegetation layer to a raster using the density attribute.
Reclassify the three density values all to 1 and the NoData areas to 0.

## Slide 25: Find landfill areas with Boolean AND
[Slope] AND [Roads] AND [Streams] AND [Vegetation]

## Slide 26: Additive model
[Slope] + [Roads] + [Streams] + [Vegetation]
Return to Outline

## Slide 27: Where do we do these calculations? Raster Calculator
Numeric formulas
Mathematical functions (sin, exp, cos, etc)
Logical operators
Boolean operators

## Slide 28: Raster analysis techniques

## Slide 29: Other raster analysis techniques
Reclassification
Surface functions
Distance functions
Density functions
Interpolation
Neighborhood functions
Zonal functions

## Slide 30: Surface analysis
DEM
Slope
Aspect
Hillshade
Contouring

## Slide 31: Slope function
Calculates slope of the surface based on surrounding cells. Can be expressed in degrees or percent.
What areas are suitable for a ski resort?

## Slide 32: Aspect function
Calculates direction of steepest slope, e.g. which way the slope “faces”. Value represents direction from 0-360 where 0/360 is North. Flat areas are assigned a -1 value.
Where should we install solar panels?

## Slide 33: Hillshade
Calculates the brightness or illumination of a surface from a specified light source.
Applications include terrain display and modeling satellite reflectance.
Azimuth is direction of illumination source (315 by default)
Altitude is the angle of the source above the horizon (45 deg)

## Slide 34: Viewshed analysis
Calculate areas visible from a set of observation points
Why is it difficult to get cell phone reception in some areas?

## Slide 35: Hydrologic functions
Derive streams, watersheds, and other hydrologic features based on analysis of a DEM.

## Slide 36: Distance functions: Lowest cost path
Create start/stop shapefiles
Create cost grid
Calculate cost distance grid and cost direction grid
Find lowest cost path

## Slide 37: Distance functions: Buffers
Roaddist < 500
Logical expressions easily create Boolean rasters representing buffers from distance rasters.

## Slide 38
How do we create a raster of the real-world from scratch?

## Slide 39
Sampling
What is sampling? A finite number of observations selected from a larger population
The earth and everything on it is comprised of an infinite number of points
It is impossible to capture every aspect of the earth – or even a small landscape – because we cannot take an infinite number of measurements
Therefore, we must measure only what is essential, or practical, or what we can afford
Source: Technics

## Slide 40
Geospatial Sampling
Sampled locations should be spaced so the “net” can capture important features
A spatial sampling interval is the average distance between sampled locations
  Short interval – more points and more detail
  Large interval – fewer points and less detail
  The sample interval should be no larger than ½ the size of the smallest detail to be mapped

## Slide 41
Geospatial Sampling
We can control 2 main aspects of the sampling process
  Choose location of samples
  Choose number of samples
Systematic sampling pattern
Usually the simplest pattern but it is not always the most efficient. One size does not always fit all.
Works best for homogeneous landscapes

## Slide 42
Systematic random sampling pattern
Random within each grid cell
Sample methods to exploit known natural patterns or features
Cluster of samples can be focused on possible hotspots
Cluster sampling – clusters focused on interest areas
Adaptive sampling – Sample location dependent on landscape (requires knowledge of landscape
Geospatial Sampling

## Slide 43
Geospatial Sampling
We can control 2 main aspects of the sampling process
  Choose location of samples
  Choose number of samples
Random sampling pattern
Grounded in statistical theory, but ignores geography
Rarely used because it is difficult to follow random pattern

## Slide 44
Geospatial Sampling
We can control 2 main aspects of the sampling process
  Choose location of samples
  Choose number of samples
Exploit your knowledge of the landscape to sample more efficiently.
If you have information about the processes that govern the landscape, then you can use that knowledge to help you design a spatial sampling pattern
Also, different layers can be built using different sampling patterns (different layers can be sampled differently)
Hybrid sampling patterns are possible